Berlin Robolabs

Project description

Robotics Control System

Revision 0.0.1
Date: 16.10.15

# Project in brief
The robotics control system, short RoCS is an open source project which aims to provide a scalable software infrastructure for robotics development. It is basically a set of Linux daemons which have the ability to communicate via a central message system.
Those messages are described by a message type and a tail containing the message data. Message data can be plain text or json structures.
Each client component is able to send messages to a queing infrastructure called rocsmq. Rocsmq is a centralized server, similar to a chat server. A client who connects it can give it a name and a filter. While the name is just for logging issues, the filter serves as a information delimiter. The server only sends messages to a client if the message type matches the filter.
All components are written in C. There is an universal logics client with the ability of tcl scripting which can be used to easily build a new component into the infratructure.
# Technical Component description
## Message queue server (rocsmq-server)

## Message queue clients
The rocsmq client is basically a set of C functions which enable the developer to connect the message queue and send or receive messages.
Additionally, there are functions for accessing dynamic linked lists as well as a function to daemonize the client process.
There is a set of standard clients which are already delivered as complete software.
### I²C Bus layer (rocsmq-i2cbus)

### CAN-Bus layer (rocsqm-canbus)

### Universal scriptable client

# Structural Overview

## Message flow

Raw data
Environmental
information
Goal
information
Control data

Hardware-Layer
Sensor-Interpreter
Logic
Action-Planner
# Handling instructions
## Prerequisities
You will need the following libraries to build rocs.
- Json-c
- libtcl
- SDL1.2 with
- SDL_net1.2
- libb64
In debian based systems you can install them using the command
apt-get install libb64-dev libsdl-dev libsdl-net1.2-dev libjson-c-dev tcl-dev

In other systems, refer to your package management system..
Note: On debian wheezy, there is no libb64 or libjson-c so you may have to compile it on your own if you use Raspbian or Bananian.

Addittionally, you will need some tools to build it.
apt-get install build-essential cmake

I hope, that's all. Tell me if not. ;)
## Building the system
To build the system, create a folder named build inside the rocs directory, change into this directory and run cmake to create the build system. After, build with make.
$ cd rocs / $ mkdir build / $ cd build / $ cmake .. / $ make

## Creating your own agents